## Slide 1
MODERN DEVELOPMENTS IN INDUSTRY · TUMA206
Water Treatment Plant
Digital Twin
A full industrial stack — field → PLC → MQTT → historian → dashboard — with an agentic AI operator assistant.
Team: [names · matriculation · cohort] · Demo day 25–26 Jun 2026

## Slide 2
THE CAPSTONE BRIEF
What we built
A working twin of a water-treatment tank that behaves like a real plant under stress — not just on the happy path. Every layer of the industrial stack is present, and an AI assistant helps the operator respond to faults.
Process twin
Tank, pumps, valve, level & pH sensors, dosing loop — physics integrated each scan.
Deterministic PLC
on/off filling, PID dosing and a state machine on a fixed scan cycle.
End-to-end data path
Tag namespace → MQTT → InfluxDB historian → Grafana dashboard.
Agentic AI assistant
Detects faults and recommends operator actions in plain language.
TUMA206 · Water Treatment Plant Digital Twin
2

## Slide 3
FIELD TO AI IN ONE STACK
Architecture
Fault injection — operator panel
one fault per layer, at runtime
Digital twin (process)
tank · pumps · valve · pH
Soft PLC
on/off · PID · state machine
sensors ⇄ commands
publish tags
MQTT broker
Mosquitto · pub/sub
Historian → InfluxDB
time-series store
AI assistant → advice
detect · recommend · explain
Grafana dashboard
live trends + alarms
TUMA206 · Water Treatment Plant Digital Twin
3

## Slide 4
LO6 — DEFEND EVERY CHOICE
Stack & justification
Layer
Choice
Why
Twin + PLC
Python, single scan loop
Transparent control logic; easy to defend in the viva.
Messaging
MQTT (Mosquitto)
Lightweight pub/sub; the de-facto IIoT transport; decouples field from IT.
Historian
InfluxDB 2.7
Purpose-built time-series DB; retention & downsampling; native Grafana link.
Dashboard
Grafana
No frontend code; provisioned trends and alarm thresholds.
AI assistant
Claude (Anthropic SDK)
Strong agentic reasoning; safe, explained advice; offline fallback.
Orchestration
docker-compose
One command brings up the whole stack — reproducible demo.
TUMA206 · Water Treatment Plant Digital Twin
4

## Slide 5
LO2 — THREE CONTROL STYLES
The twin & its control
One PLC scan cycle reads sensors, runs the logic, writes actuators — at a fixed period, like real hardware.
O
On/off Inlet pump fills the tank with hysteresis between low/high level setpoints.
P
PID Dosing pump regulates pH to setpoint with anti-windup integral clamping.
S
State machine FILLING → TREATING → DISCHARGING phases sequence the batch.
Twin physics: level from a mass balance (inflow − outflow), pH a first-order lag toward the dosing equilibrium — stable and explainable.
TUMA206 · Water Treatment Plant Digital Twin
5

## Slide 6
LO3 — FIELD TO DASHBOARD
Tags & the data path
Every value is a named tag with a unit and type — the single source of truth all services share.
Example tags
LIT101_level tank level · m
AIT201_ph tank pH
FIT101_inlet_flow influent flow · m³/s
P101_inlet_cmd / _run_fb command + feedback
P201_dose_cmd PID dosing output 0–1
PLC_state state-machine phase
LIT101_predicted mass-balance estimate
Field device
Soft PLC
MQTT broker
InfluxDB historian
Grafana dashboard
TUMA206 · Water Treatment Plant Digital Twin
6

## Slide 7
LO4 — ONE FAULT PER PURDUE LAYER
Fault catalog
Layer
Fault
Detection signal
Sensor
Level transmitter stuck
Diverges from mass-balance prediction
Equipment
Inlet pump runs, no flow
Command + feedback ON while flow ≈ 0
Process
pH excursion
Setpoint deviation beyond alarm band
Infrastructure
MQTT broker / data loss
Telemetry staleness watchdog
TUMA206 · Water Treatment Plant Digital Twin
7

## Slide 8
FAST, DETERMINISTIC, EXPLAINABLE
Detection approach
Analytical redundancy
A stuck sensor diverges from an independent estimate (mass balance). A dead pump leaves both flat — that's how we tell them apart.
Command vs effect
A running motor contactor doesn't prove flow. Comparing command to measured flow catches mechanical failure.
Setpoint deviation + debounce
pH alarms only after the deviation persists, so transient noise doesn't trip false alarms.
Staleness on time, not value
When all tags go quiet at once it's a data outage — not a process alarm. Operators must not chase a phantom.
TUMA206 · Water Treatment Plant Digital Twin
8

## Slide 9
LO5 — RECOMMEND & EXPLAIN, SAFELY
The AI operator assistant
1
Detect
Rule-based checks raise a fault from sensor cross-checks and trends — independent of the LLM.
2
Recommend
Claude receives the fault + a recent tag snapshot and returns diagnosis, actions and reasoning as JSON.
3
Explain & advise
Plain-language guidance grounded in the data — the agent advises, a human decides.
Safety & resilience — the agent never actuates; it must ground claims in the data it was shown; and if the API is unavailable it falls back to a built-in playbook so the live demo always produces advice.
TUMA206 · Water Treatment Plant Digital Twin
9

## Slide 10
DETECT + ALERT + ADVISE ≤ 60 S
Demo day flow
For each of the four faults, injected live from the operator panel:
1
Inject — operator panel publishes the fault to the control topic
2
Twin reacts — physics + PLC respond; the fault propagates through the stack
3
Detect & alarm — rule engine raises the fault; Grafana shows the trend break
4
AI recommends — assistant posts diagnosis + actions, all within 60 seconds
TUMA206 · Water Treatment Plant Digital Twin
10

## Slide 11
EXPECT VIVA QUESTIONS HERE
Design decisions & trade-offs
Detect deterministically, then ask the LLM
Guarantees the ≤60 s requirement even if the model is slow or offline; the LLM adds the reasoning, not the trigger.
MQTT over OPC-UA
Simpler and lighter; we accept losing OPC-UA's richer typed metadata.
First-order physics, not CFD
Enough fidelity to make control loops and faults realistic, while staying explainable.
InfluxDB over plain SQL
Time-series native: retention, downsampling and Grafana integration out of the box.
Agent advises, never actuates
Human-in-the-loop is the safe pattern for an operator assistant.
TUMA206 · Water Treatment Plant Digital Twin
11

## Slide 12
Thank you
Questions on any part of the system — we can walk through the code.
Repo: github.com/[team]/wtp-digital-twin · Live demo: docker compose up